SuperPosition – Rev 1
Bill of Materials
Function / Name	#	Note	Part Number
MCU Teensy 3.5/3.6	1	Cut USB power trace	DEV-14057
Display OLED SSD1306	1	SSD1306 / SPI / 0.96’’ / 128x64 [1]
Adafruit NeoTrellis	1	4x4 RGB LED Button Matrix [2]	Mouser: 485-1616
Silicone 4x4 Keypad	1	Silicone Elastomer Button Keypad [3]	Mouser: 485-1611
Rotary Encoder	2	24 Pulse Mechanical Rotary Encoder	PEC11R-4220F -S0024
Tactile Switch	2	9.4mm Black Button Tactile Switch	2-1825910-7
3.5mm Jacks	12	“Thonkiconn” Mono Jacks from Thonk	PJ398SM
DAC MCP4922	2	12-bit Digital to Analog Converter	MCP4922-E/P
Op-amp MCP6004	1	Operational Amplifier	MCP6004-E/P
Op-amp TL04CN	2	Operational Amplifier	TL074CN
Regulator L7805	1	5V Voltage Regulator	L7805CP
Diode 1N5817	2	Through Hole	1N5817
Resistor 100k SMD 0805	24	0.1%
Resistor 56k SMD 0805	4	0.1%
Resistor 1k SMD 0805	8	1%
Capacitor 10u SMD 0805	2	Ceramic Capacitor
Capacitor 100n SMD 0805	6	Ceramic Capacitor

[1] https://www.amazon.co.uk/IZOKEE-Display-SSD1306-Raspberry-White-IIC/dp/B076PKKTRP/ref=sr_1_fkmr0_1?keywords=ssd1306%2Bspy%2B0.96%27%27&qid=1557409352&s=electronics&sr=1-1-fkmr0&th=1
[2] https://www.adafruit.com/product/3954
[3] https://www.adafruit.com/product/1611
Build Guide (work in progress)
1. Solder the 2 10u 0805 SMT Capacitors in the front;
2. Solder the 6 100n 0805 SMT Capacitors in the back;
3. Solder all the 0805 SMT Resistors in the back;
4. Solder the 1N5817 Diodes in the back;
5. Solder the L7805 Voltage Regulator in the back;
6. Solder the Power Header in the back;
7. Solder the pin sockets for the teensy in the back;
8. Solder the ICs in the front (MCP6004, TL074CN, MCP4922);
9. Solder the buttons and encoders in the front;
10. Solder all of the jacks on the top;
11. Solder the Adafruit NeoTrellis PCB in the front;
12. Solder the OLED Display in the front;
13. Place the Panel on the front of the PCB;
14. Cut the USB power trace on the back of the teensy;
15. Place the teensy on the back;